## Slide 1
WELCOMES
AP GENCO, VJA
ENGINEERS
B.S.N.L. AP CIRCLE.,
VIJAYAWADA

## Slide 2: Services of BSNL
Services
Voice
Data
Wireline
Wireless
Wireline
Wireless

## Slide 6: About Business in INDIA TELECOM
No. of Mobile Customers in India = 132 Cr
No. of Landlines working in India = 3 Cr
No. of Data Customers in India = 82 Cr
Business Turn-over in India = Rs 400000 Cr per annum

## Slide 7
SALIENT FEATURES
EMPLOYABILITY
(a) Telecom Manufacturing side
(B) Telecom
operations side

## Slide 14: 60% of present day IT projects are Telecom Software developments

## Slide 15
DATA SERVICES

## Slide 17
NIC CARD

## Slide 24
Dynamic IP 112.211.192.16
Static IP 204.15.23.255
Facebook
user
Server

## Slide 25
TELECOM EXAMPLES
Telephone Exchange

## Slide 26
TELECOM EXAMPLES
Server Point
Branch office

## Slide 27
27
NOC
switch
NOC
switch
NOC
switch
NOC
switch
BRAS
BRAS
BRAS
BRAS
Caching server
Caching server
Tier-1 switch
Tier-1 switch
Tier-1 switch
Tier-1 switch
Tier-2 switch
Tier-2 switch
Tier2-switch
Tier-2 switch
Tier-2 switch
DSLAM
DSLAM
DSLAM
DSLAM
DSLAM
CPE
CPE
CPE
CPE
CPE
CPE
CPE
CDN NOC CENTRE
ADSL
DATA CENTRE
M P L S
CDN Network with MPLS
Multicasting
IGMP snooping / PIM-DM

## Slide 28
Broadband Equipment

## Slide 29: Current MPLS Core
CHENNAI
MUMBAI
KOLKATTA
NAGPUR
BANGALORE
JALLUNDHAR
JAIPUR
NEW DELHI
CHANDIGARH
DEHRADUN
NOIDA
JOTHPUR
AHMEDABAD
RAJKOT
LUCKNOW
AHMEDABAD
PATNA
GUWAHATI
RANCHI
JABALPUR
RAIPUR
BHUBANESWAR
INDORE
PUNE
HYDERABAD
VIJAYAWADA
BELGAUM
MANGALORE
ERNAKULAM
COIMBATORE
A1 Node
A2 Node
A3 Node
A4 Node

## Slide 31
B1+B2=73
A4=10
A3=6
A2=3
A1=5

## Slide 32: Internet cloud
INDIA

## Slide 33
DSLAM
DSLAM
DSLAM
DSLAM
Tier-2 switch
Tier-2 switch
BRAS
BRAS
POINT OF PRESENCE

## Slide 34: MPLS VPN

## Slide 35: Internet Cloud

## Slide 36
BSNL

## Slide 39
UNDER OCEAN OF CABLES

## Slide 40: Network Architecture
B
T
S
MSC VLR
HLR
AUC
EIR
PSTN
ISDN
(
Air interface
OSS
B
T
S
B
T
S
MSC VLR
BSC
1 MSC=16 BSC
1 BSC=1024 TRU
A Interface
A-bis interface
BSC:BASE STATION CONTROLLER, BTS: BASE TRANSRECEIVER STATION, OSS: OPERATION AND SUPPORT SUBSYSTEM.ss

## Slide 41: 3G rel99 Architecture (UMTS) - 3G Radios
SS7
IP
BTS
BSC
MSC
VLR
HLR
AuC
GMSC
BSS
SGSN
GGSN
PSTN
PSDN
CN
C
D
Gc
Gr
Gn
Gi
Abis
Gs
B
H
BSS Base Station System
BTS Base Transceiver Station
BSC Base Station Controller
RNS Radio Network System
RNC Radio Network Controller
CN Core Network
MSC Mobile-service Switching Controller
VLR Visitor Location Register
HLR Home Location Register
AuC Authentication Server
GMSC Gateway MSC
SGSN Serving GPRS Support Node
GGSN Gateway GPRS Support Node
A
E
PSTN
2G MS (voice only)
2G+ MS (voice & data)
UMTS Universal Mobile Telecommunication System
Gb
3G UE (voice & data)
Node B
RNC
RNS
Iub
IuCS
ATM
IuPS
Notes: 41

## Slide 42
AP BSNL INTRANET IP ASSIGNING
TO CONNECT TO INTERNET, USER NEED UNIQUE IP

## Slide 44
I.P. V4

## Slide 45: Definition of IP Address
* “A unique string of decimal numbers
separated by full stops that identifies
each computer using the Internet
Protocol to communicate over a
network.”
* It is a Four Fielded Octet
* It indicates Network
* It indicates Host
* Ex : 121.25.122.2

## Slide 46: Dmins
AP BSNL INTRANET IP ASSIGNING

## Slide 47: IP required for
(1) Website Administrators
(2) Static IP Users
(3) Internet Service Providers for Internet
(4) Corporate/Entrepreneurs for Intranet
(5) Networking Engineers
(6) Research & Development

## Slide 48
Dynamic IP 112.211.192.16
Static IP 204.15.23.255
Facebook

## Slide 49: IP Addresses
Hostname gmail.com have IP Address 74.125.79.83
The following IP address ranges belong to Facebook:
66.220.144.0 - 66.220.159.255
69.63.176.0 - 69.63.191.255
204.15.20.0 - 204.15.23.255
All IP addresses belonging to "WhatsApp Inc", that were looked up on this site.
50.22.210.151 3/06/2015 1:01:23AM 208.43.244.170 3/06/2015 12:49:46 AM

## Slide 51: If I have many more Systems in a larger area

## Slide 52: Limited Hosts

## Slide 53: What is an IP address?
Each host on a TCP/IP network is uniquely identified at the IP layer with an address.
The IP address is also known as Protocol address
The IPv4 address is 32 bits long
2^32=4294967296=429Cr

## Slide 54
Country | Country Code | Addresses(million) | Per Capita
United States | US | 1474.319 | 5.297
China | CN | 194.425 | 0.152
Japan | JP | 153.327 | 1.210
European Union | EU | 114.103 | -
Germany | DE | 85.300 | 1.038
Canada | CA | 76.197 | 2.446
South Korea | KR | 72.239 | 1.542
United Kingdom | GB | 70.795 | 1.187
France | FR | 68.385 | 1.155
Australia | AU | 37.378 | 1.979
Italy | IT | 32.344 | 0.561
Brazil | BR | 29.755 | 0.175
Russian Federation | RU | 24.919 | 0.170
Taiwan | TW | 24.681 | 1.109
Netherlands | NL | 21.249 | 1.339
Sweden | SE | 18.998 | 2.144
India | IN | 18.312 | 0.018
Notes: 54

## Slide 55
Where do IP addresses come from?
Standards
Allocation
Allocation
Assignment
End user
Regional Internet Registries (RIRs)
distribute IPv4, IPv6, and AS numbers
to the Internet community
RIRs maintain accurate registration of
Internet resource usage for the community
IANA : Internet Assigned Numbers Authority
IETF : Internet Engineering Task Force
Notes: 55

## Slide 56
Regional Internet Registries
1992: “…it is [now] desirable to consider delegating the registration function to an organization in each of those geographic areas.” (RFC 1338)
Notes: 56

## Slide 57: Who Are the IP Address Provisioning Organizations?
ICANN | Allocate to RIRs =Regional Internet Registries Internet Corporation for Assigned Names and Numbers (ICANN) Internet Assigned Numbers Authority [IANA]
RIR | Allocate to Service Providers Assign to Enterprises The Asia Pacific Network Information Centre
NIR/LIR/ISP | Reallocate to Service Providers Reassign to Enterprises
AFRINIC, APNIC,
ARIN, LACNIC,
RIPE NCC
IANA

## Slide 58: IPv4 Address Scheme
How we see an IP address? 140.179.220.220
What the Internet machines see an IP address? 11001010000011100100000000000001
For human understanding the 32 bits of IP address are separated into 4 bytes of 8 binary digits
Each binary byte is converted into decimal and is separated by a dot hence also known as Dotted Decimal Notation

## Slide 59: IPv4 Address Scheme
In decimal the address range is 0.0.0.0 to 255.255.255.255
The IP address is of the form <networkID,hostID>
8 Bits
8 Bits
8 Bits
8 Bits
Network Host
32 Bits
172 . 16 . 122 . 204

## Slide 60: If there are many systems in a Company?

## Slide 61: IPv4 Address Scheme
There are five classes of addresses A, B, C, D & E.
A, B & C classes are used to represent host and network address.
Class D is a special type of address used for multicasting.
Class E is reserved for experimental use.

## Slide 62: IPv4 Address classes
H
H
H
N
Class-A:
H
H
N
N
Class-B:
H
N
N
N
Class-C:
Class-D:
For Multicast
Class-E:
For Research
N=Network number assigned by IANA
H=Host number assigned by network administrator.

## Slide 63: IPv4 Address Scheme
Class:A : 0-127 . 0-255 . 0-255 . 0-255
Class:B : 128-191 . 0-255 . 0-255 . 0-255
Class:C : 192-223 . 0-255 . 0-255 . 0-255
Class:D : 244-239 . 0-255 . 0-255 . 0-255
Class:E : 240-255 . 0-255 . 0-255 . 0-255
The IP address is of the form <networkID,hostID>
8 Bits
8 Bits
8 Bits
8 Bits
0-127 [=126N]
128-191 [=64N]
192-223 [=32N]
224-239 [=16N]
240-255 [=16N]

## Slide 64: IP Address Bit Patterns
8 Bits
8 Bits
8 Bits
8 Bits
Class-A:
Class-B:
Class-C:
Class-D:
Class-E:
0-127 [=126N]
128-191 [=64N]
192-223 [=32N]
224-239 [=16N]
240-255 [=16N]
0 0 0 0 0 0 0 0
1 0 0 0 0 0 0 0
1 1 0 0 0 0 0 0
1 1 1 0 0 0 0 0
1 1 1 1 0 0 0 0
0 1 1 1 1 1 1 1
1 0 1 1 1 1 1 1
1 1 0 1 1 1 1 1
1 1 1 0 1 1 1 1
1 1 1 1 1 1 1 1

## Slide 65: Identifying a class of address by a machine
Address Identifier
Network Address
Host Address
0
7 bits Network Address
24 bits Host Address
A
10
14 bits Network Address
16 bits Host Address
B
110
21 bits Network Address
8 bits Host Address
C
1110
Multicast address (224.0.0.0-239.255.255.255)
D
1111
Reserved for future use
E

## Slide 66: Class-A address (Networks)
Number of Networks = 27 i.e.128 (0-127)
Network ID ‘0’ is not used.
Network ID ‘127’ is reserved for loop back and is used for internal testing.
Number of Networks = 126
Network IDs = 1-126
hhhhhhhh
hhhhhhhh
hhhhhhhh
0nnnnnnn
Network
Host
0
7 bits Network Address
24 bits Host Address

## Slide 67: Class-A address (Hosts)
Number of Networks = 27 i.e.128
Number of Hosts=224=16777216
No Host ID can have all zeros i.e. 0.0.0 and specifies network address.
No Host ID can have all ones i.e. 255.255.255 and specifies the broadcast address.
Number of Hosts per network= 224 -2=16777214
hhhhhhhh
hhhhhhhh
hhhhhhhh
0nnnnnnn
Network
Host
0
7 bits Network Address
24 bits Host Address

## Slide 68: Class-B address
Number of Networks = 214 i.e.16384
Number of Hosts = 216 i.e. 65,536 (0-65,535)
No Host ID can have all zeros i.e. 0.0 and specifies network address.
No Host ID can have all ones i.e. 255.255 and specifies the broadcast address.
Number of Hosts per network= 216 -2=65534
nnnnnnnn
hhhhhhhh
hhhhhhhh
10nnnnnn
Network
Host
10
14 bits Network Address
16 bits Host Address

## Slide 69: Class-C address
Number of Networks = 221 i.e. 2097152
Number of Hosts = 28 i.e. 256 (0-255)
No Host ID can have all zeros i.e. 00000000 and specifies network address.
No Host ID can have all ones i.e. 11111111 and specifies the broadcast address.
Number of Hosts = 28-2 = 254
nnnnnnnn
nnnnnnnn
hhhhhhhh
110nnnnn
Network
Host
110
21 bits Network Address
8 bits Host Address

## Slide 70: Class-D & E addresses
Class D are special addresses are known as multicast addresses
This address is assigned to a group of networks and not to represent a unique address
This address is used to send IP datagrams to a group but not to all the hosts on the network
This address is also used to address router update messages
1110
Multicast address (224.0.0.0-239.255.255.255)
1111
Reserved (240.0.0.0-255.255.255.255)

## Slide 71: Networks Vs Hosts
In Classless environment we can have 232=4294967296 Hosts
Class Networks Hosts/Network
A 126[128-2] 16777214 [256x256x256(-2)]
B 16382 [=64x256(-2)] 65534 [256x256(-2)]
C 2097150 [32x256x256 (-2] 254 [256-2]
So, In Cl-A : [Appr 211 cr]
In Cl-B : [Appr 107 cr]
In Cl-C : [Appr 53 cr] Total = 371 Cr

## Slide 72: Address space utilisation
0
1
0
127
00000000
01111111
A-50%
1
0
128
191
10000000
10111111
B-25%
0
1
192
223
11000000
11011111
C-12.5%
240
255
11110000
11111111
E-6.25%
0
224
239
11100000
11101111
D-6.25%
0
1
100%

## Slide 73
Classes of IP addresses are identified by the decimal number of the 1st octet
Class A address begin with a 0 bit
Range of class A addresses = 0.0.0.0 to 127.255.255.255
Class B address begin with a 1 bit and a 0 bit
Range of class B addresses = 128.0.0.0 to 191.255.255.255
Class C addresses begin with two 1 bits & a 0 bit
Range of class C addresses = 192.0.0.0 to 223.255.255.255.

## Slide 74: Reserved Addresses
Network address: It is used to identify the network itself.
Broadcast address :Used to broadcast packets to all devices on a network.

## Slide 75: Private IP addresses
Class A - 10.0.0.0 to 10.255.255.255
Class B - 172.16.0.0 to 172.31.255.255
Class C - 192.168.0.0 to 192.168.255.255

## Slide 76
AP BSNL INTRANET IP ASSIGNING

## Slide 77
SUB NETTING

## Slide 78: Subnetting
•Creating Multiple independent Networks from a Single Network.
•Converting Host bits into Network Bits
i.e. Converting 0’s into 1’s
•Subnetting can be performed in two ways.
–FLSM (Fixed Length Subnet Mask)
–VLSM (Variable Length subnet mask)
•Subnetting can be done based on requirement .
  – Requirement of Networks ?
  –Requirement of Hosts ?

## Slide 79: Default subnet mask
•Subnet Mask differentiates Network portion and Host Portion
•Represented with all 1’s in the network portion and with all 0’s in the host portion.

## Slide 80: Default subnet mask
Class A : N.H.H.H
11111111.00000000.00000000.00000000
Default Subnet Mask for Class A is 255.0.0.0
Class B : N.N.H.H
11111111.11111111.00000000.00000000
Default Subnet Mask for Class B is 255.255.0.0
Class C : N.N.N.H
11111111.11111111.11111111.00000000
Default Subnet Mask for Class C is 255.255.255.0

## Slide 81: How Subnet Mask Works ?
IP Address:192.168.1.1
Subnet Mask:255.255.255.0
ANDING PROCESS:
192.168.1.1 = 11000000.10101000.00000001.00000001
255.255.255.0 = 11111111.11111111.11111111.00000000
=======================================
192.168.1.0= 11000000.10101000.00000001.00000000
=======================================
Hence, 192.168.1.0 is the Network Address.
The output of an AND table is 1 if both its inputs are 1.
For all other possible inputs the output is 0

## Slide 82: Requirement of Networks is 4 ?
Class C : N.N.N.H110xxxxx.xxxxxxxx.xxxxxxxx.xxxxxxxxClass C : 192.168.1.0
•No. of Subnet=2^n >=4
Req. of Subnet=2^2 >=4
n=2
No. of Host=2^h –2
[“-2” is for Network ID & Broadcast ID]
=2^6 –2=64 –2=62 Hosts/Subnet

## Slide 83
Actual Octet Format in Class-C:
N.N.N.00000000
=> N.N.N.ΦΦ000000 [ Since, n=2 ]
There are 6 Zeros,
No. of hosts=26-2=64-2=62 Hosts/Subnet
So, There are 4 subnets and 62 Hosts per each subnet.

## Slide 84: If Subnet Mask is 255.255.255.192 , Then New Networks and respective hosts are :
192.168.1.00000000= 192.168.1.0 [I Subnet]
192.168.1.01000000= 192.168.1.64 [II Subnet]
192.168.1.10000000= 192.168.1.128 [III Subnet]
192.168.1.11000000= 192.168.1.192 [IV Subnet]
Ranges : 192.168.1.0 to 192.168.1.63=>64 IDs
192.168.1.64 to 192.168.1.127 =>64 IDs
192.168.1.128 to 192.168.1.191 =>64 IDs
192.168.1.192 to 192.168.1.255 =>64 IDs

## Slide 85: Now subnet Mask :
N.N.N.ΦΦ000000
=>11111111. 11111111. 11111111.11000000
=>255 .255 .255 . (128+64)+0+0+0+0+0+0+0
=>255 .255 .255 .192
[ It can be understood like this:
NID = All 1’s, SID= All 1’s, HID=All 0’s]
[For, 9 subnets, 128+64+32=224]

## Slide 86
In 192.168.1.0 to 192.168.1.63
192.168.1.0 is Network ID & 192.168.1.63 is Broadcast ID
Hence, there are 62 IDs for host in First Subnet
In 192.168.1.64 to 192.168.1.127
192.168.1.64 is Network ID & 192.168.1.127 is Broadcast ID
Hence, there are 62 IDs for host in Second Subnet
In 192.168.1.0.128 to 192.168.1.191
192.168.1.128 is Network ID &192.168.1.191 is Broadcast ID
Hence, there are 62 IDs for host in Third Subnet
In 192.168.1.192 to 192.168.1.255
192.168.1.192 is Network ID &192.168.1.255 is Broadcast ID
Hence, there are 62 IDs for host in Fourth Subnet

## Slide 87: Range of IP addresses
192.168.1.0 -- 192.168.1.63 /26
192.168.1.64 – 192.168.1.127 /26
192.168.1.128 – 192.168.1.191/26
192.168.1.192 – 192.168.1.255 /26
Similarly in Class – A and Class – B also.,

## Slide 88: Now subnet Mask :
N.N.N.Φ0000000
=>11111111. 11111111. 11111111.10000000
=>255 .255 .255 . (128)+0+0+0+0+0+0+0+0
=>255 .255 .255 .128
[ It can be understood like this:
NID = All 1’s, SID= All 1’s, HID=All 0’s]
[For, 9 subnets, 128+64+32=224]

## Slide 89: Now subnet Mask :
N.N.N.ΦΦΦ00000
=>11111111. 11111111. 11111111.11100000
=>255 .255 .255 .128+64+24+0+0+0+0+0+0
=>255 .255 .255 .224
[ It can be understood like this:
NID = All 1’s, SID= All 1’s, HID=All 0’s]
[For, 9 subnets, 128+64+32=224]
[For, 16 subnets, 128+64+32+16=240]

## Slide 90
I.P. V6

## Slide 91: IPv6
To meet the continual growth of the Internet, IETF has proposed a set of specifications commonly known as the next generation IP protocol (“IPng” or IPv6”).
IPv6 increases the address size from 32 bits to 128 bits, supporting up to 3.4X1038 nodes.
It is represented using hexadecimal values separated by colons using the format X:X:X:X:X:X:X:X:, where each X refers to a four digit hexadecimal integer (16 bits each).
One such address could be BA98:7654:3210:FEDC:BA98:7654:3210:0043.

## Slide 92: Problems of IPv4
Addressing problem
Routing Crisis
End to End problem
Security
Mobility
Performance
Cost

## Slide 93: Address Crisis

## Slide 94: Routing Crisis

## Slide 95: End to End problem

## Slide 96: Mobility

## Slide 97: Security Problem

## Slide 98
  Larger address space
  Global reachability
  Flexibility
  Auto-configuration
  Aggregation
  Multi-homing
  Efficient Routing
  Scalability
  Easy Mobility
  Better security
IPv6 Features

## Slide 99: IPv6
No more room in IPv4
Quite empty in IPv6

## Slide 100: Larger Address Space
Notes: Autoconfiguration allows a host to automatically join a ipv6 network upon startup.

## Slide 101: Global Reachability
From 32 bits to 128 bits addresses enables:
– Global reachability:
• No hidden networks, hosts
• All hosts can be reachable and be "servers"
Notes: Autoconfiguration allows a host to automatically join a ipv6 network upon startup.

## Slide 102: Flexibility
From 32 bits to 128 bits addresses enables:
– Flexibility
Notes: Autoconfiguration allows a host to automatically join a ipv6 network upon startup.

## Slide 103: Auto-Configuration
• "Plug and play"
– By autoconfiguration
Notes: When a network is connected to many ISPs , the technique is called Multi homing.
IPv6 multihoming is required to preserve the scalability of the interdomain routing system. A proposed method is to assign multiple provider-dependent aggregatable (PA) IPv6 prefixes to each site, instead of a single provider-independent (PI) prefix.
Autoconfiguration & renumbering features are defined in RFC 2462

## Slide 104: Aggregation
• Aggregation
Notes: When a network is connected to many ISPs , the technique is called Multi homing.
IPv6 multihoming is required to preserve the scalability of the interdomain routing system. A proposed method is to assign multiple provider-dependent aggregatable (PA) IPv6 prefixes to each site, instead of a single provider-independent (PI) prefix.
Autoconfiguration & renumbering features are defined in RFC 2462

## Slide 105: Multi-homing

## Slide 106: Efficient Routing

## Slide 107: Scalability

## Slide 108: Easy Mobility

## Slide 109
End to End Security

## Slide 110: Better Security
X
X

## Slide 112: 4 digit Hexadecimal Integer
Minimum : 000016 = 02 = 010
Maximum : ffff16 = 1111 1111 1111 11112
= 6553510

## Slide 113
12/11/2023
IPV4 Address (Present)
IPV6 Address (Future)
Total Addresses = 2^32 = 4 billion
Some addresses are reserved for special purposes like private networks or multicast addresses. However practically only 250 million addresses are usable.
Total Addresses = 2^128 = 340 billion, billion, billion, billion
IP Address Schemes
Notes: 113

## Slide 116
Decimal equivalent of ffff is 65535
So,
65535x65535x65535x65535x65535x65535x65535x65535
= 3.4x 1038 = 340 x 1036
= 340 Trillion Trillion Trillion

## Slide 119
Introduction to Routers

## Slide 120: Router fundaments
The router is a device that connects two networks
A router accepts packets on at least two network interfaces and forwards packets from one interface to another.
A router works at network layer.
Each router maintains a database called routing table of the router
This routing table contains network addresses.
Routers do not talk to remote computers

## Slide 121: Router fundamentals
Router is like a PC and has
  Mother board
  CPU
  Memory
  Ports & interfaces to hook peripherals
  May have a monitor to serve as a console
Types of routers
Hardware routers
      Cisco, juniper, nortel , dlink, DAX
Software routers
      Microsoft server , LINUX server

## Slide 122: CISCO’s HIERARCHICAL DESIGN MODEL
Access Layer : Small organization
Ex:1600,1700,1800,2500 series
Distribution Layer: Medium size organization
ex: 2600,2800,3600,3700,3800
Core layer : Very large organizations and ISPs.
ex:7200,7600,10000,12000

## Slide 123: Cisco 1600,1700,1800,2500 series Routers

## Slide 124: 2600,2800,3600,3700,3800 series routers

## Slide 125: :7200,7600,10000,12000 routers

## Slide 126: 7200,7600,10000,12000 routers

## Slide 127: EDGE ROUTER

## Slide 130: Interfaces of routers
LAN Interface to connect to the switch
WAN Interface to connect to the next router (serial port)
Administrative port (console port)
Auxiliary port

## Slide 131: DIFFERENT PORTS

## Slide 132: Types of WAN technologies
Leased Line
MLLN(Managed leased line network)
ISDN
MPLS
Broadband

## Slide 133: Routing and Routing Protocols
Introduction to Static Routing

## Slide 134: Routing Methods
Routers must learn the direction to remote networks in order to forward packets.
Two ways to learn this information:
  Dynamically
    Information is learned from other routers
      Often through RIP, OSPF, or EIGRP routing protocols
  Statically
    Configured manually
      Requires the network administrator to add and delete static routes when topology changes
      In large networks it requires a tremendous amount of administrative time
      On small, or unchanging networks, it requires very little maintenance

## Slide 135
Static Routing
Routes for each destination network has to be manually configured by the administrator.
Used in small networks.
Route may be up or down but static routes will remain in the routing tables and traffic would still be sent towards the route
Not suitable for large networks

## Slide 136: Static Route Operation
Static route operations can be divided into 3 stages:
  A network administrator manually configures the static route on the router
  The router installs the route in its routing table
  Packets are routed using the static route

## Slide 137: Configuring Static Routes
Send traffic through an interface:
Send traffic to the next router’s address:
Destination Network
Subnet Mask
Next Hop IP Address (address of next router)
Destination Network
Subnet Mask
Local Router’s Outgoing Interface

## Slide 138: Configuring the Outbound Interface

## Slide 139: Configuring the Next-Hop Address

## Slide 140: Static Routes as Backups
Often static routes are used for backup purposes, such as when the dynamically learned route fails.

## Slide 141: Backup Route Example
For Router0, the preferred path to the 192.168.0.0 network is through the switch.
192.168.0.0/24
192.168.1.1
192.168.1.2
192.168.2.1
192.168.2.2
No Routing Protocol

## Slide 142
Dynamic Routing
  Changes in the network topology are updated dynamically.
  Only the directly connected networks information is required for configuration.
  Administrative work is reduced.
  It is used in medium and large networks.
  RIP & OSPF are routing protocols

## Slide 145: Intra-AS Routing
Also known as Interior Router Protocols (IRP) or Interior Gateway Protocols (IGP)
Most common:
  RIP: Routing Information Protocol
  OSPF: Open Shortest Path First
  IGRP: Interior Gateway Routing Protocol (Cisco proprietary)

## Slide 147
147
Routing Updates
After exchanging 2 periodic updates, the network is converged.
10.1.2.0
10.1.1.0
10.1.3.0
10.1.4.0
.2
.1
.2
.1
.1
.2
A
B
C
10.1.4.0 10.1.2.2 2
10.1.1.0 10.1.3.1 2
10.1.3.0 10.1.2.2 1
10.1.1.0 10.1.2.1 1
10.1.2.0 10.1.3.1 1
NW VIA HOP
10.1.1.0 ---------- 0
10.1.2.0 ---------- 0
NW VIA HOP
10.1.2.0 ---------- 0
10.1.3.0 ---------- 0
NW VIA HOP
10.1.3.0 ---------- 0
10.1.4.0 ---------- 0
Routing Table-A
Routing Table-B
Routing Table-C
10.1.4.0 10.1.3.2 1

## Slide 148
Hop Count
  A hop count metric simply count router hops.
  From router-A it is 1 hop to network 192.168.5.0 if packets are sent out interface 192.168.3.0 and 2 hops if sent out 192.168.1.0
A
B
C
192.168.1.0
192.168.7.0
192.168.6.0
192.168.5.0
192.168.2.0
192.168.3.0
192.168.4.0

## Slide 149: OSPF “advanced” features (not in RIP)
Selects high Bandwidth route
Security: all OSPF messages authenticated (to prevent malicious intrusion); TCP connections used
Multiple same-cost paths allowed (only one path in RIP)
For each link, multiple cost metrics for different Type Of Service (e.g., satellite link cost set “low” for best effort; high for real time)
Integrated uni- and multicast support:
  Multicast OSPF (MOSPF) uses same topology data base as OSPF
Hierarchical OSPF in large domains.

## Slide 150
Bandwidth
  A bandwidth metric would choose a higher bandwidth over a lower bandwidth.
  A packet from router A to C will follow path A-B-C.
A
B
C
192.168.1.0
192.168.7.0
192.168.6.0
192.168.5.0
192.168.2.0
192.168.3.0
192.168.4.0
A-C: 64kbps
A-B: 2mbps
B-C: 2mbps

## Slide 151: IGRP (Interior Gateway Routing Protocol)
CISCO proprietary; successor of RIP (mid 80s)
Distance Vector, like RIP
Several cost metrics (delay, bandwidth, reliability, load etc)
Uses TCP to exchange routing updates
Loop-free routing via Distributed Updating Alg. (DUAL) based on diffused computation

## Slide 152
MPLS

## Slide 158: PACKET FORMAT

## Slide 160
Traditional

## Slide 161: Overview of MPLS Forwarding

## Slide 162: Typical example of MPLS
1
2
Ingress Routing Table
Destination
Next Hop
134.5/16
200.3.2/24
(2, 84)
(3, 99)
MPLS Table
In
Out
(1, 99)
(2, 56)
MPLS Table
In
Out
(3, 56)
(5, 0)
3
5
2
3
134.5.1.5
200.3.2.7
200.3.2.1
134.5.6.1
Destination
Egress Routing Table
Next Hop
134.5/16
200.3.2/24
134.5.6.1
200.3.2.1
200.3.2.7
99
200.3.2.7
0
200.3.2.7
200.3.2.7
56
200.3.2.7
5

## Slide 170: MPLS Terminology
Forwarding Equivalence Class (FEC)— The group of packets are forwarded in the same manner over the same path with the same forwarding treatment.
LER (Label edge router)---Boarder routers of MPLS domain where the adding or removing of the label will be taking place. These are also called as edge routers.
LSR (Label switched router)---These are the high speed routers in the core of the MPLS N/W. These are also called as core routers. These routers will swap the labels.

## Slide 171: Any Doubts Please…..!

## Slide 172: THANK YOU