## Slide 1
Presentation on
U-NMS
for
ISTS & State Utility Communication Network
In
U-NMS and ISTS Communication System

## Slide 2: Background
CERC notified Communication Regulation in May’17 which envisaged Centralized Supervision System for ISTS Communication.
As per CERC notification- CTU shall be the Nodal Agency for implementation of system for centralized supervision for quick fault detection and restoration of ISTS Communication.
Technical standard & Manual of Communication Planning Criteria being finalized by CEA envisage requirement of System for centralized supervision for ISTS Communication.
Guidelines framed by NPC for Availability Calculation of Communication envisage System for centralized supervision for ISTS Communication
Accordingly, POWERGRID has worked out Scheme for implementation of U-NMS System for centralized supervision of Communication network for Southern Region including ISTS & State Utilities. The agenda was discussed in the 160th OCC meeting held on 15.10.2019 and it was decided that further deliberation is required on subject matter.

## Slide 3: Present Scenario
POWERGRID took up implementation of ISTS Communication as part of Schemes i.e. ULDC, SR FO Expansion and SR Reliable in Southern Region.
Network Management Systems(NMS) for SDH & PDH for maintenance of Communication System came up as part of the project.
Supplied NMSs are proprietary in nature managing the ISTS communication of implemented nodes.
There are multiple NMSs for SDH & PDH are available in Southern Region working in isolation.
Majority of ISTS Communication nodes implemented by other utilities are not integrated with existing NMSs as they were implemented in different projects.
Present NMSs were considered with requirement mainly for monitoring and maintenance of implemented Communication Nodes.
In light of Communication Regulation 2017 certain provisions are envisaged for ISTS Communication for which existing NMSs are not capable.
Centralized Management of ISTS Communication in the present scenario needs State of the Art NMS for Centralized Management of ISTS Communication.
To meet these objectives, Unified Network Management System (U-NMS) at National and Regional level are conceived for managing Communication System.

## Slide 4: Proposed U-NMS Scheme
Centralised Management of ISTS Communication System at Regional and National levels by integrating existing NMSs and Network Elements (which are remotely accessible or having standard & open APIs). The U-NMS Scheme shall consist of Centralised Application Server acquiring data of Communication nodes from multiple NMSs in the region as well as from NEs.
The proposed U-NMS shall acquire data directly from existing NMSs of ISTS and State Utility and also from nodes not integrated with existing NMS for all ISTS and all other Utility communication links. The system shall be designed for managing Intra State, ISTS, Inter-Regional Communication Systems for State, Regional and National level respectively.
U-NMS Configuration for National & Regional shall consist of Servers, Storage Devices, VPS, Switches, Routers, Firewall, Remote workstations, Printer, Furniture etc. in dual LAN in Main (High Availability-HA) and Backup configuration to manage ISTS regional, inter-regional and Cross Border communication links.
U-NMS Configuration for managing Intra State Communication for SLDCs shall also be considered by providing Remote workstations, Furniture etc. with rights to access servers of respective RLDCs to manage their respective Communication Network.

## Slide 5: Benefits of Scheme
Availability of Communication System through Centralized U-NMS system for entire ISTS & State Communication in a region for efficient management
Visibility of all ISTS & State Utility Communication Nodes in single NMS.
State of the Art UNMS with advance features such as availability calculations, fault report generation for inter-patched network, centralised configuration, Provisioning, Quick Fault detection Restoration, Analytics, data retention for two calendar years plus the current year for all interfaces in the network etc., to meet challenges post Communication Regulations scenario.

## Slide 6: U-NMS Project Proposal
Centralised Network Management System for National, Regional and State Level Communication Networks to be taken up in unified manner for effective management of Communication System.
Configuration consisting Application Servers, Work Stations, VPS, Web Server, Fire Wall and required Peripherals for Regional and National (and EMS/ NMS Server as required)
Workstation based Control Centre at State level with VPS/ TV Screen and peripherals
Estimated cost- Rs. 100 Crs. for SR and Rs 600 Crs for all regions including National (excluding AMC cost and Civil Works)
Implementation Schedule: 24 Months from date of Investment Approval
The scheme shall be implemented by POWERGRID on tariff route basis and
investment to be recovered as per CERC notification.
Members may deliberate the scheme for consideration of approval.

## Slide 7: Communication Regulation 2017…..
Quote:
….
4. OBJECTIVE:
These regulations provide for planning, implementation, operation and maintenance and up-gradation of reliable communication system for all communication requirements including exchange of data for integrated operation of National Grid.
5. SCOPE and APPLICABILITY:
(i) These regulations shall apply to the communication infrastructure to be used for data communication and tele -protection for the power system at National, Regional and inter-State level and shall also include the power system at the State level till appropriate regulation on Communication is framed by the respective State Electricity Regulatory Commissions.
(ii) All Users, SLDCs, RLDCs, NLDC, CEA, CTU, STUs, RPCs, REMC, FSP and Power
Exchanges shall abide by the principles and procedure as applicable to them in accordance with these regulations.
6. NODAL AGENCY:
(i) The nodal agency for planning, and coordination for development of communication system for inter-State transmission system user shall be the Central Transmission Utility.
(ii) The nodal agency for planning, and coordination for development of communication system for intra - State transmission system user shall be the State Transmission Utility.
(vii) CTU shall be the Nodal Agency for supervision of communication system in respect of inter-State communication system and will implement centralized supervision for quick fault detection and restoration.
…..
Unquote

## Slide 8
Centralised Supervision for Communication System
Typical Function of U-NMS
The main goals of U-NMS shall be as follows:-
Provide the point of integration across multi-vendor, multi technology network equipment and network management systems.
Provide an end-to-end view of services and service performance (quality), and an end-to-end view of the bearer circuits that carry services.
Provide Auto discovery and Rediscovery of network elements and its subsystems, like hardware inventory, ports, protection and topological links and circuits.
Provide Graphical representation of topology of nodes and links.
Provide creation of resource inventory of physical and logical network components.
Provide creation of service inventory of circuits.
Provide detection of addition/deletion in the network and reconciliation of network with inventory data.
Provide facility for end to end provisioning of bandwidth centrally.
Enable fast fault resolution and reduced restoration times through accurate fault localization and notifications to the appropriate repair centers.
Enable proactive maintenance and customer support through detecting early signs of impending equipment failures and service faults.
Provide accurate, near-real-time service- and network-status information.
Provide information for long distance network (bandwidth) availability.
Automatically protect long distance traffic depending on priority.

## Slide 9
Centralised Supervision for Communication System
Typical Function of U-NMS
            The scope for the U-NMS Package shall be for Supply, Installation, customization, commissioning, training, Operation and maintenance of centralized NMS (U-NMS) and documentation for countrywide transmission network, as per the requirement specified in different sections of the Technical Specifications, with following major features:
Service Fulfillment:
  Network Resource Management (Network Discovery , Inventory Management & Reconciliation)
  Design, Assign, Activation/Provisioning, Configuration and Re-Engineering
Service Assurance:
  Fault Management System
  Performance Management System
  User Security Management
Common Module:
Order Management System
Helpdesk for trouble ticketing /Web Portal
MIS Reporting & Dash Boarding System
Infrastructure:
Servers, Storage, Switches (LAN and SAN), Routers, Firewall etc.
Backup & Restoration Feature
(Applications/ Functions may vary for National/ Regional/ State depending upon the Operational / Administrative Requirements)